## Slide 1
EDGE-LLM CODEC
A Compression-Aware Hardware Pipeline for Deploying LLMs on Flash / DRAM / SRAM-Constrained Edge Devices
Honours Project • Qwen3-8B → SparseGPT + AWQ-4bit + QAT/QAFT → Tile-wise Zstd → HW Codec

## Slide 2
THE PROBLEM
Dense 8B-class LLMs don't fit edge silicon, even after pruning and quantization
BF16 Dense
~16 GB
Pruned + AWQ-4bit
~5-6 GB
Edge NPU budget
tens of MB SRAM
+ a few GB DRAM
Even at 4-bit, weights alone overflow edge flash/DRAM budgets — and the KV cache keeps growing with every generated token. Compression can't be an offline afterthought: it has to be a first-class stage of the inference datapath itself, with dedicated hardware to decompress weight tiles and to compress/decompress the KV cache in real time.
Edge-LLM Codec | Motivation

## Slide 3
SOFTWARE PIPELINE (COMPLETE)
Qwen3-8B
Dense BF16 baseline
SparseGPT
One-shot Hessian pruning
AWQ 4-bit
Activation-aware quant
QAT / QAFT
Accuracy recovery
Tile-wise Zstd
3 compressed streams
Tile-wise Zstd splits into three independently compressed streams:
Attention weight tiles
Q / K / V / O projections
FFN / MoE expert tiles
gate, up, down projections (8-expert SMEAR)
KV cache tiles
generated at runtime — compressed dynamically, see next slides
Why tile-wise, not model/layer/tensor-wise? Bounds SRAM working set to one tile, bounds decode latency so it hides behind compute, and lets the accelerator start consuming a tensor before it fully arrives from flash.
Edge-LLM Codec | Software Pipeline

## Slide 4
HARDWARE PIPELINE (THIS STAGE)
Two complementary accelerators close the loop between compressed storage and the compute array
Decompression Accelerator
static weight tiles
OPERATES ON
Attention + FFN/MoE weight tiles
DIRECTION
Flash/DRAM → SRAM → MAC array
TIMING
Prefetch-driven, pipelined ahead of compute
CODEC
Tile-wise Zstd: tANS/FSE entropy + LZ77 match stage
Compression Accelerator
dynamic KV cache
OPERATES ON
KV cache tiles (K, V per token per layer)
DIRECTION
Attention output → DRAM, and back
TIMING
Must keep up with per-token decode latency
CODEC
Same KV-cache Zstd library, run in reverse (encode)
Both accelerators share a common decode-side core (tANS/FSE decode, match reconstruction, AXI-style DMA, double-buffered tile scheduler) — the KV-cache path only adds a forward encode datapath on top.
Edge-LLM Codec | Hardware Overview

## Slide 5
DECOMPRESSION ACCELERATOR
Real-time weight-tile reconstruction — flash/DRAM to MAC array
Tile Fetch / DMA
+ Scheduler
Sequence Decoder
(LZ77 stage)
Entropy Decode
(FSE / tANS core)
Dequant / Format
Reconstruction
Double-Buffered
Output SRAM
Flash / DRAM
MAC Array (Shrutam-2 / Sooktam)
Tile granularity co-designed with compression-ratio-vs-latency analysis — small enough to decode within one MAC pass, large enough to amortize header overhead
Entropy decode is variable-rate: output FIFO or wide multi-symbol lookup absorbs the “bubble cycle” problem seen in Huffman/ANS hardware decoders
MoE-aware prefetch: only decompress tiles for routed experts (8-expert SMEAR FFN), not the full weight set
Reuses the tANS decode core, AXI DMA, and double-buffer scheduler from the prior general-purpose Zstd accelerator design
Edge-LLM Codec | Decompression Accelerator

## Slide 6
COMPRESSION ACCELERATOR
Real-time KV-cache compression — the dynamic half of the codec, in the per-token critical path
WRITE PATH (compress new K/V)
Tile
Accumulator
Quantize
(K: per-ch / V: per-tok)
Match Finder
(small window)
FSE/tANS
Table Build + Encode
Writeback
to DRAM
READ PATH (decompress for attention — reuses decompression core)
Tile Fetch
/ DMA
Sequence
Decoder
FSE/tANS
Decode
Dequant
(K per-ch / V per-tok)
Attention
Unit
Latency budget is per-token, not per-tile-fetch — unlike weight decompression, there is no long prefetch window to hide behind
Open question: adaptive / precomputed FSE tables vs. per-tile table build, to bound encode latency at decode token rate
K and V are quantized asymmetrically (per-channel / per-token) — matches the offline KV-cache library for bit-exact compatibility
Edge-LLM Codec | Compression Accelerator

## Slide 7
TARGET PLATFORMS & STATUS
Shrutam-2
Conformer encoder + Llama-architecture decoder, 8-expert SMEAR MoE FFN, structured 2:4 sparsity, INT8-normalized mixed-precision MAC arrays
Sooktam
Companion NPU project sharing the same compressed-weight streaming interface
PROJECT STATUS
✓
Dense baseline established (Qwen3-8B)
✓
SparseGPT pruning
✓
AWQ 4-bit quantization
✓
✓
Offline tile-wise Zstd compression (3 streams)
Decompression accelerator RTL (weights)
Compression accelerator RTL (KV cache)
Integration with Shrutam-2 / Sooktam datapath
Real-time throughput / latency characterization
Edge-LLM Codec | Platforms & Status